## Slide 1: Tutorial 1 Basics Of NS-3
Creation of Nodes and facilitating communication between them in Point to Point Network

## Slide 2: Getting started
Create a .cc file in ns-3.20/scratch.
Include the appropriate headers.
To display data on your command/terminal screen use LOG Components.
  NS_LOG_COMPONENT_DEFINE (“Title");
  NS_LOG_INFO ("Creating Topology");
  LogComponentEnable ("UdpEchoClientApplication", LOG_LEVEL_INFO);

## Slide 3: Steps to follow
Include the header files of the functions that you want to use.
  #include "ns3/core-module.h"
  #include "ns3/point-to-point-module.h"
  #include "ns3/network-module.h"
  #include "ns3/applications-module.h“
using namespace ns3; //necessary
Start your coding in int main() module

## Slide 4: Inside main()
Use the command line code to see the python graphical window:
  CommandLine cmd;
  cmd.Parse (argc,argv);
Create nodes:
  NodeContainer p2pNodes; //where p2pnodes is the node container i.e. //object of the class NodeContainer
  p2pNodes.Create (<number of nodes>); //Create is the function defined in //the class NodeContainer
Specify how you want to connect the nodes
  Wired network
    LAN, Point-to-Point,etc
  Wireless network
    Wifi(802.11),etc.

## Slide 5
Example:Wired Point to point network
  PointToPointHelper pointToPoint;
  pointToPoint.SetDeviceAttribute ("DataRate", StringValue ("1Kbps"));
  pointToPoint.SetChannelAttribute ("Delay", StringValue ("2ms"));
Create a NetDeviceContainer object to use its function called install, to get the properties of the network i.e. pointToPoint in the above case and give them to p2pNodes.
  NetDeviceContainer p2pDevices;
  p2pDevices = pointToPoint.Install (p2pNodes);

## Slide 6
Install the internet stack into your nodes:
  InternetStackHelper stack;
  stack.Install (p2pNodes);
Give address to your nodes:
  Ipv4AddressHelper address;
  address.SetBase ("10.1.1.0", "255.255.255.0");
  Ipv4InterfaceContainer p2pInterfaces;
  p2pInterfaces = address.Assign (p2pDevices);

## Slide 7
Assign the Client and the servers for transport layer i.e TCP/UDP. Below code is for UDP:
  uint16_t port = 9; // well-known echo port number
  UdpEchoServerHelper server (port);
  ApplicationContainer apps = server.Install (p2pNodes.Get (1));
  apps.Start (Seconds (1.0));
  apps.Stop (Seconds (10.0));
  uint32_t packetSize = 1024;
  uint32_t maxPacketCount = 1;
  Time interPacketInterval = Seconds (1.);
  UdpEchoClientHelper client (serverAddress, port);
  client.SetAttribute ("MaxPackets", UintegerValue (maxPacketCount));
  client.SetAttribute ("Interval", TimeValue (interPacketInterval));
  client.SetAttribute ("PacketSize", UintegerValue (packetSize));
  apps = client.Install (p2pNodes.Get (0));
  apps.Start (Seconds (2.0));
  apps.Stop (Seconds (10.0));

## Slide 8
As we don’t have routing protocol for the above case directly populate the tables.
  Ipv4GlobalRoutingHelper::PopulateRoutingTables ();
Create Pcap file that can be analysed using wireshark.
  pointToPoint.EnablePcapAll (“<pcap_file_name>");
Create trace file that can be analyzed using Trace Metrices(optional)
  AsciiTraceHelper ascii;
  Ptr<OutputStreamWrapper> osw = ascii.CreateFileStream ("fin.tr");
  phy.EnableAsciiAll (p2pNodes);
Include these commands to run your program
  Simulator::Run ();
  Simulator::Destroy ();

## Slide 9
Using your terminal window enter the directory ns-3.20
To run your program that is in scratch use:
  ./waf --run scratch/<program_name> --vis
  Use vis if you want to visualize the movement of nodes.
Use Wire Shark/Trace Metrices to analyse the Pcap/trace files.